SECTION 07 18 13 PEDESTRIAN TRAFFIC COATING

SECTION 07 54 19 POLYVINYL-CHLORIDE ROOFING

REVISED July 26 / 2017

Copyright © 2008 - 2017 Tuff Industries Inc. All rights reserved

** NOTE TO SPECIFIER

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by one of the following methods:

Microsoft Word 2007: Click the OFFICE button, select WORD OPTIONS select DISPLAY, than select or deselect the HIDDEN TEXT option.

Microsoft Word (earlier versions): From the pull-down menus select TOOLS, then OPTIONS. Under the tab labeled VIEW, select or deselect the HIDDEN TEXT option.

Corel WordPerfect: From the pull-down menus select VIEW, then select or deselect the HIDDEN TEXT option.

** Tuff Industries, Inc.; Waterproof Traffic Membranes.
 .
 This section is based on the products of Tuff Industries, Inc., which is located at:
 9570 Bottom Wood Lake Rd.
 Lake Country, BC, Canada V4V 1S7.
 Toll Free Tel: (877) 860-9333.		Tel: (250) 766-1333	Fax: (250) 766-1366.
 Email: info@tuffindustriesinc.com					Web: www.tufdek.com  

Tufdek is a waterproofing system available in a variety of colors and designs for above grade wood or concrete decks, patios and walkable roof areas.

Tufdek “walking deck and roof systems” are suitable for waterproofing horizontal surfaces over habitable and inhabitable spaces subject to pedestrian traffic.

Tufdek - 2 Ply walkable roof systems: Base membrane consisting of “Tufdek TX 60 mil base sheet fully adhered to the substrate then capped with Tufdek 61 mil walking deck membrane which is fully adhered to the base sheet and hot air welded at the perimeters.

PART 1

GENERAL

  - SECTION INCLUDES

** NOTE TO SPECIFIER ** Delete one of items (A or B) below not required for project.

    - Waterproof vinyl traffic membrane, single-ply, walkable roof surface.

    - Waterproof vinyl traffic membrane, two-ply walkable roof surface.

    - Waterproof vinyl traffic membrane for the following applications:

      - Balcony decks.

      - Roof decks.

      - Walkways.

      - Ramps.

      - Stairways.

      - Patios.

      - Above grade court yards.

      - Above grade swimming pool deck.

      - Hot tub decks.

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

    - Section 03 30 00 - Cast-In-Place Concrete: Concrete flooring to receive vinyl decking.

    - Section 06 16 00 - Sheathing: Subfloor plywood or cementitious underlayment to receive vinyl decking.

    - Section 06 20 13 (subsection) – Exterior Finish Carpentry: Moldings and trims at floor penetrations and terminations.

    - Section 07 18 13 (subsection) - Pedestrian Traffic Coatings.

    - Section 07 54 19 (subsection) – Polyvinyl-Chloride Roofing.

    - Section 07 60 00 – Flashings and Sheet Metal.

    - Section 07 70 00 – Roof and Wall Specialties and Accessories: Scuppers, drains counter flashings and reglets.

  - REFERENCES

** NOTE TO SPECIFIER ** Delete references from the list below that are not actually required by the project specifier.

    - ASTM D 4434 - 09 Standard Specifications for (Polyvinyl Chloride) Sheet Roofing. Tufdek reports: Trinity / ERD Report # 02732.09.04 / project 02750.06 LAB.

    - CCMC 07544 - Canadian Construction Materials Centre. Polyvinyl Chloride Roofing and Waterproof Membranes, "PVC Sheet - Applied Roofing" Type 4, Class B. Tufdek listing # 13293-L.

    - CAN/CGSB 37.54-95 - Canadian General Standards Board Standard for Roofing and Waterproofing Membrane, Sheet Applied, Flexible Polyvinyl Chloride. Tufdek Trinity / ERD report # P2770.05.07 - R1.

    - Intertek (Warnock Hersey) Certification, Quality Control and License to Mark as per Tufdek report # 3124471. Listed on www.spec-direct.com

    - QAI fire testing: Tufdek test report RJ3782 – 1 - Rev 1, ASTM E108-11 Class C fire rating and Tufdek test report RJ3782 – 2 - Rev 2, ASTM E108-11 Class A fire rating.

    - Trinity ICC-ES AC39 Sections 4.13.4 and 4.15 (Wind Uplift and Impact Resistance). Tufdek test report # T32800.08.10.

    - ICC-ES – AC39 / AC75 Systems used as coverings in walking decks and non-classified roof covering systems over concrete and plywood substrates.             Tufdek test report # ESR 3262

  - DESIGN REQUIREMENTS

    - Drainage:

      - Slope: 1/4 inch in 12 inches (6mm in 305mm) recommended.

      - Direction: Slope towards drain or drainage point.

      - Ponding Water: Exterior decks should slope away from the building to a drain or drainage point. Decks shall be designed and constructed to avoid excessive water ponding, the responsibility of which lies with the design professional having authority of the project and not the waterproofing contractor. Some incidental ponding after a rain is to be expected and is not covered under warranty. Standing water exceeding the following shall be rectified:  6 mm (1/4”) in depth that exceeds 1.0 square meter (10.76 square feet) and remains standing in excess of 72 hours after a rainfall has stopped on days of evaporation. The standing water must be a result of rainfall, some retained water at drains, deck edges, seams, transitions or flashing is not uncommon and is not considered an installation defect or warranty issue.

    - Structural:

      - Tufdek membranes are acceptable for use with structures designed to support lightweight deck / roof assemblies.

      - Adequacy of the structural support must be verified by the owner or the owner's technical representative and is their sole responsibility to determine.

      - Potential live loads, such as snow or ponding water, should be considered.

    - Acceptable Substrate:

1. 	Minimum 5/8" exterior grade Fir plywood.

2. 	Minimum 5/8” Tolko T-Ply Pro or Ultra T & G plywood subfloor.

3. 	Minimum 1/2” PermaBase, cementitious underlayment.

    - Chemical Compatibility:

      - Tufdek membranes must not come in contact with bitumen or tar based products.

      - Tufdek membranes must not come in contact with pressure treated wood.

      - Tufdek membranes must not come into contact with polystyrene insulations.

      - Tufdek membranes must not come in contact with copper based metals, water runoff from copper can discolor the surface of the membrane.

      - Tufdek membranes can be affected by chemicals found in commercial / residential environments. Many chemicals left to absorb into the membrane and / or then exposed to extreme heat or ultra violet light can cause permanent discoloration or damage to Tufdek membranes. Contact Tuff Technical Department for question related to chemical incompatibilities.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Product Data: Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

    - Detail Drawings: Submit copies of manufacturer's standard detail drawings describing installation methods, seaming plan showing joints, termination details and interface with other materials as well as flashing conditions applicable to the project.

** NOTE TO SPECIFIER ** Delete selection samples if colors have already been selected.

    - Selection Samples: For each finish product specified two complete sets of color samples 8 1/2 inches by 11 inches (216mm x 280mm), representing manufacturer's full range of available colors and patterns.

    - Verification Samples: For each finish product specified, two samples, minimum size 6 inches by 4 inches (152 mm x 102 mm) square representing actual product, color, and patterns.

    - Installer's qualifications.

  - QUALITY ASSURANCE

    - Manufacturer Qualifications: All primary products specified in this section will be supplied by a single manufacturer with a minimum of ten (10) years experience.

    - Installer Qualifications: All products listed in this section are to be installed by an installer with a minimum of two (2) years demonstrated experience installing products of the same type and scope as specified.  Installer must have completed the factory training or have been trained by an authorized dealer who has completed the factory training.

** NOTE TO SPECIFIER ** Include a mock-up if the project size and/or quality warrant taking such a precaution. The following is one example of how a mock-up on a large project might be specified. When deciding on the extent of the mock-up, consider all the major different types of work on the project.

    - Mock-Up: Provide a mock-up for evaluation of surface preparation techniques and application workmanship.

      - Finish areas designated by Architect.

      - Do not proceed with remaining work until workmanship, color, and details are approved by Architect. Refinish mock-up area as required to produce acceptable work.

      - Pre Installation Meeting: Discuss waterproof practices and precautions applicable to this project.

  - DELIVERY, STORAGE, AND HANDLING

    - Store products in manufacturer's unopened packaging until ready for installation.

    - Store and dispose of hazardous materials, and materials contaminated by hazardous materials, in accordance with requirements of local authorities having jurisdiction.

    - Deliver all materials to the job site in their original, tightly-sealed container or unopened packaging.

    - All materials must be clearly labeled with the manufacturer's name and product identification.

    - All materials must be protected from damage during transit, handling, storage and installation. Leave all materials on pallets fully protected from moisture.

    - Reject damaged materials at delivery. Replace all damaged materials with new materials.

    - All materials shall be stored in a dry area and protected from the elements. Store membrane rolls flat on pallets.

    - Store adhesive at temperatures between 5 C (40 F) and 26 C (80 F): if adhesives are exposed to lower temperatures, verify usability with manufacturer before using.

    - Store all flammable materials in a cool, dry area away from sparks and open flames. Follow precautions outlined by manufacturer / supplier.

  - AMBIENT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, dew point and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's absolute limits.

  - WARRANTY AND MAINTENANCE

    - At project closeout, provide to Owner or Owners Representative a copy of the manufacturer's current standard limited warranty against manufacturing defect, outlining its terms, conditions, and exclusions from coverage. Include a copy of the manufacturer’s current Tufdek membrane maintenance instructions.

- PRODUCTS

  - MANUFACTURERS

Acceptable Manufacturer: Tuff Industries Inc, located at:

9570 Bottom Wood Lake Rd; Lake Country, BC, Canada V4V 1S7;

Toll Free: 877-860-9333; Email: info@tufdek.com Web: www.tufdek.com

** NOTE TO SPECIFIER ** Delete one of the following, (A or B); coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions: Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - APPLICATIONS/SCOPE

    - Apply vinyl flooring over all “light foot” traffic bearing decks and roof decks in commercial, institutional and residential applications; restoration and new construction.

    - Fully adhered vinyl flooring without ballast to solid construction, suspended concrete or fir plywood, on flat, sloped and unusual configuration traffic decks.

** NOTE TO SPECIFIER ** Delete the following paragraph (2.3 of 2-ply system) if not required.

  - BASE SHEET MEMBRANE FOR TUFDEK 2-PLY SYSTEM

    - Base Sheet Membrane:

      - Membrane Overall Thickness: Tufdek TX 60 mil, (1.53 mm).

      - Sheet Width: 64.25 inches (1625.6 mm) typical; other standard widths as applicable to project requirements and available from the manufacturer.

      - Weight: 1653 g/m2.

      - Elongation Tear Strength - ASTM D 751: PASS.

      - Dimensional Change - CGSB 37.54-95: PASS.

      - Accelerated Weathering - ASTM G 154 at 5000 hours: PASS.

      - Color: TX white top, black back. Product can have either side facing up.

  - TRAFFIC MEMBRANE

** NOTE TO SPECIFIER ** Select specified membrane, one of (A or B) and delete the other. Modify the included text as instructed.

    - Supreme Tufdek Waterproof Traffic Membrane:

      - Membrane Overall Thickness: 61 mil, (1.55 mm).

      - Sheet Width: 64.25 inches (1632 mm); other standard widths as applicable to project requirements may be available from the manufacturer.

      - Weight: 1653 g/m2.

      - Seam Strength - CGSB 37.54-95: PASS.

      - Elongation Tear Strength - ASTM D 751: PASS.

      - Dimensional Change - CGSB 37.54-95: PASS.

      - Accelerated Weathering - ASTM G 154 at 5000 hours: PASS.

** NOTE TO SPECIFIER ** Select membrane color. Delete all others.

      - Color: Graphite

      - Color: Pearl

      - Color: Walnut

      - Color: Almond

      - Color: Desert Sand

      - Color: Slate Grey

      - Color: Valencia Marble

      - Color: Sanibel Marble

      - Color: Carrara Marble

    - Designer Tufdek Waterproof Traffic Membrane:

      - Membrane Overall Thickness: 61 mil, (1.55 mm).

      - Sheet Width: 64.25 inches (1632 mm); other standard widths as applicable to project requirements may be available from the manufacturer.

      - Weight: 1653 g/m2.

      - Seam Strength - CGSB 37.54-95: PASS.

      - Elongation Tear Strength - ASTM D 751: PASS.

      - Dimensional Change - CGSB 37.54-95: PASS.

      - Accelerated Weathering - ASTM G 154 at 5000 hours: PASS.

** NOTE TO SPECIFIER ** Select membrane color. Delete all others.

      - Color: Aggregate

      - Color: Birch

      - Color: Rustic Plank

      - Color: Driftwood

  - ADHESIVES

** NOTE TO SPECIFIER ** Select Adhesive. Delete any of the following not required of (A, B, C,).

    - Tuff – “Trowel On”: Water-based synthetic polymer trowel on adhesive used for bonding all Tufdek membranes to flat horizontal wood surfaces, Shelf life 1 Year.

    - Tuff – “Low VOC Contact Adhesive”: Solvent based, roll or brush on adhesive for bonding all Tufdek membranes to flat or vertical wood and / or concrete surfaces. Shelf life 1 Year.

** NOTE TO SPECIFIER ** Delete sub item (1) if 2-ply system not required.

      - Used for adhering Tufdek top ply to base ply in the Tufdek 2 ply system.

    - Tuff – “Roll-On”: Water-based synthetic polymer roll on adhesive used for bonding all Tufdek membranes to flat horizontal or vertical wood and / or concrete surfaces, Shelf life 1 Year.

  - ACCESSORIES

    - Tuff – “Deck Patch”: Cement based floor leveling compound used for filling plywood gaps, knotholes and uneven surfaces, follow directions for mixing on container.

** NOTE TO SPECIFIER ** Retain only Accessories required on this project and delete all others. Modify the included text where instructed.

    - Tuff-Seal Drain: Spun aluminum drain with PVC coated flange and removable clamping ring.

    - Tuff-Seal Overflows: Welded aluminum overflows with PVC coated flange and a 12 inch (304.8 mm) outflow pipe.

** NOTE TO SPECIFIER ** Select Overflow Drain Diameter. Delete all others.

      - Drain Diameter: 2 inch (50.8 mm) o.d. (sloped at 10%).

      - Drain Diameter: 3 inch (76.2 mm) o.d. (sloped at 10%).

      - Drain Diameter: 2 inch (50.8 mm) i.d. (sloped at 0%).

      - Drain Diameter: 3 inch (76.2 mm) o.d. (sloped at 0%).

    - Tuff-Clad H/D PVC Metal: 21 mil unreinforced membrane laminated to 24 gauge G-90 Galvanized steel fabricated by contractor into metal flashings and edge details.

** NOTE TO SPECIFIER ** Select One Tuf-Clad PVC Flashing Membrane Color. Delete all others.

      - Color: Stone.

      - Color: Wicker.

      - Color: White.

      - Color: Black.

      - Color: Sand.

    - Tuff-Seal Box Scuppers: All aluminum construction with PVC coating and welded exit pipe. 4 by 4 by12 inches (101 by 101 by 305 mm).

- EXECUTION

  - EXAMINATION

    - Do not begin installation until substrates have been properly prepared.

    - If substrate preparation is the responsibility of installer, notify Architect of unsatisfactory preparation before proceeding.

  - SUBSTRATE PREPARATION

It is the Installation contractor’s responsibility to ensuring the substrate is acceptable for the Tufdek system

A. Correct Substrate Defects.

1. 	Defects that need to be corrected before work can commence should be brought to the attention of the General Contractor or Owner in writing and addressed by them.

2. 	For re-decking applications, remove existing waterproof system components as specified by the project designer. If components are discovered during installation that could be detrimental to the performance of the new Tufdek system, they should be brought to the attention of the Project Designer, General Contractor or Owner for corrective action.

3.	 If soundness and integrity of the existing structure cannot be verified, good practice requires a complete tear-off for inspection and repair. However, recovering an existing structure is an alternative to removing all existing components. Non- destructive testing, in conjunction with core cuts, must be completed to determine the condition of the existing structure.

4. 	The installation contractor is responsible for assuring that all wet substrate materials are dry prior to the installation of the new waterproof system.

5.	 In the absence of a Design Professional or General Contractor, the Installation Contractor should coordinate with the building owner to assure conditions are satisfactory to commence with the project as designed.

B. Remove Moisture

1. 	Ponded water, snow, frost and/or ice, must be removed from the work surface(s) and completely dried prior to installing the Tufdek System.

C. Prepare Surface

1. 	Acceptable substrates to which the Tufdek System is installed must be properly prepared prior to the system installation. The surface must be relatively even, clean, dry, smooth, free of sharp edges, fins, loose or foreign materials, oil, grease and other materials that may damage the system. Rough surfaces that could cause damage to the membrane must be repaired as determined by the Design Professional.

D. Fill Voids

1. 	All surface voids of the immediate membrane substrate greater than 1/4” (6.35 mm) wide must be filled.

** NOTE TO SPECIFIER ** Delete section (3.3) if 2-ply system is not required.

  - FULLY-ADHERED TUFDEK TX 60 "BASE PLY" MEMBRANE FOR TWO – PLY SYSTEM

    - Unroll the TX 60 membrane and position without stretching. Allow the membrane to relax for 15 minutes if the temperature is above 60 F (15 C), or at least 30 minutes if temperature is lower. Inspect membrane, remove or replace any product that is creased or damaged.

    - Lap sheets a minimum of 1.0 inch / 25.4 mm (minimum) or per acceptable standard roof practice to allow for a continuous weld area leaving room for adjustments and trimming of seams if necessary.

    - Fold back one half the width of the membrane and apply Tufdek adhesive in accordance with the manufacturers written instructions. Upon proper curing of the recommended adhesive roll membrane into the adhesive and push out air as to not create wrinkles or bubbles under the membrane. Fold back the remaining half, and repeat the process.

    - Refer to all manufacturer's instructions / specifications or contact Tufdek Technical Department for requirements.

    - Hot-air weld all seams with a continuous nominal 1.0 inch / 25.4 mm (minimum) weld width or per acceptable standard roof practice.

    - Inspect all welded seams for continuity and integrity using a seam probe, rounded screwdriver or similar blunt object. Seam checks are to be made daily by the contractor.

  - FULLY-ADHERED MEMBRANE

    - Unroll the Tufdek membrane and position without stretching. Allow the membrane to relax for 15 minutes if the temperature is above 60 F (15 C), or at least 30 minutes if temperature is lower. Inspect membrane, remove or replace any product that is creased or damaged.

    - Lap sheets a minimum of 1.0 inch / 25.4 mm (minimum) weld width or per acceptable standard roof practice to allow for a continuous weld area leaving room for adjustments and trimming of seams if necessary.

** NOTE TO SPECIFIER ** Delete sub section (1) if 2 ply system not required.

      - For 2 ply system, stagger the seams on the top ply to ensure they are not directly on top of the base ply seams; to avoid build up of materials.

    - Fold back one half the width of the membrane and apply Tufdek adhesive in accordance with the manufacturers written instructions. Upon proper curing of the recommended adhesive roll membrane into the adhesive and push out air as to not create wrinkles or bubbles under membrane. Fold back the remaining half, and repeat the process.

    - Refer to all manufacturer's instructions / specifications or contact Tufdek Technical Department for further information.

    - Hot-air weld all seams with a continuous nominal 1.0 inch / 25.4 mm (minimum) weld width or per acceptable standard roof practice.

    - Inspect all welded seams for continuity and integrity using a seam probe, rounded screwdriver or similar blunt object. Seam checks are to be made daily by the contractor.

  - FLASHINGS

    - Install Tuff-Clad PVC metal and / or membrane flashings and hot air weld 1.0 inch / 25.4 mm (minimum) or per acceptable standard roof practice to all metal and membrane flashings.

    - Install all flashings concurrently with the membrane as Work progresses.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION